## Slide 1: Digital Electronics(18EC34)
By
Mrs Kokila K S
Asst Prof
Dept of ECE ,BGSIT

## Slide 2
Introduction
to
Logic Gates

## Slide 3: What are Logic Gates?
Description …
Basic building blocks of a digital circuit
Data processing on the circuit is controlled using transistors
Output depends on the logic gate and the input
Input is one of two states – high or low
Output is one of two states – high or low
There are seven types of logic gates

## Slide 4: What are Logic Gates?
There are three basic types of logic gate.
AND gate
OR gate
NOT gate

## Slide 5: The AND Gate
Symbol

## Slide 6: The AND Gate

## Slide 7: The OR Gate
OR Gate

## Slide 8: The OR Gate

## Slide 9: The NOT Gate
The logical inverter

## Slide 10: The NOT Gate

## Slide 11: Thinking in Binary
+
-
YES
TRUE
1
NO
FALSE
0
HIGH
LOW

## Slide 12: True or False?
The AND Gate
TRUTH TABLE
A
B
Q
A
B
Q
0
0
0
0
1
0
1
0
1
1
1
0

## Slide 13: True or False?
The OR Gate
TRUTH TABLE
A
B
Q
A
B
Q
0
0
0
0
1
1
1
0
1
1
1
1

## Slide 14: True or False?
The NOT Gate
TRUTH TABLE
A
Q
A
Q
0
1
1
0

## Slide 15: Combining Logic Gates
An AND gate and a NOT gate
A
B
C
Q

## Slide 16: Combining Logic Gates
NAND gate
A
B
C
Q

## Slide 17: Combining Logic Gates
An AND and
NOT Gate (NAND)
TRUTH TABLE
A
B
C
Q
A
B
C
Q
0
0
0
0
1
0
1
0
0
1
1
1
1
1
1
0
Q = NOT (A AND B)