## Slide 1
PART A
DESIGN OF RCC STRUCTURES
Chapter 1
DESIGN OF COMBINED FOOTINGS

## Slide 2: Combined footings are constructed for two or more columns when they are close to each other and their foundations overlap.
Combined | footings are | provided
only when |  | 
1. When | two columns | are close
together, causing overlap of adjacent isolated footings
Where soil bearing capacity is low causing overlap of adjacent isolated footings.
Proximity of building line or existing building or sewer, adjacent to building column.

## Slide 3
The main purpose of using combined footing is to distribute uniform pressure under the footing.
To achieve this , the center of gravity of the footing area should coincide with the center of gravity of the two columns loads.

## Slide 4: Following are the different types of combined footing
9
Slab type combined footing
Slab and Beam type combined footing
Strap type Combined footing.

## Slide 5
Design a combined footing for two RCC columns A and B separated by distance of 4 m c/c, Column A is 500 x 500 and carries a load of 1250 KN and Column B is 600 x 600 and carries a load of 1600 KN. Take SBC of soil as 200 KN/m2 . Use M20 concrete and Fe415 Steel. Draw the rough sketches of the following
  Sectional Elevation
  Plan of bottom reinforcements
  Plan of top reinforcements
  Cross Section of two different places to show the maximum details of shear reinforcements.
Data Given :
Size of Column A = 500 x 500 mm Load on Column A W1 = 1250 KN Size of Column B = 600 x 600 mm Loan on Column B W2 = 1600 KN
2
SBC of Soil = 200 KN/m
fck = 20 KN/m2 fy = 415KN/m2
Soln:
1. Size of the Footing:
Total Column Load =
1250 + 1600 = 2850 KN
Self Wt. of Footing = 10 % of Column Load = 285 KN
Total load = 3135 KN

## Slide 6
Area of footing L X B =
𝑇𝑜𝑡𝑎𝑙 𝐿𝑜𝑎𝑑
𝑆𝐵𝐶 𝑜𝑓 𝑆𝑜𝑖𝑙
=
3135
200
Af = L x B = 15.675 m2
Assume the Width of the footing between 1.5 m to 2.5 m Take B = 2.5 m
L x B = 15.675
L =
15.675
2.5
 Provide L x B =
= 6.27 m say 6.5 m
6.5 m x 2.5 m
2. Projections p1 & p2:
Projections should be such that the center of gravity of column loads should coincide with the center of the footing.

## Slide 7
 CG of footing from the center of the Column A
x̄ =
(𝑊1∗𝑥1 ) + (𝑤2∗𝑥2)
(𝑊1+𝑊2)
=
(1250∗0 ) + (1600∗4)
(1250+1600)
x̄ = 2.24 m
From the above diagram ,we can write
p1 + 2.24 = L/2 p1 + 2.4 = 6.5/2
p1 = 1 m Also p1 + 4 + p2 = L
1 + 4 + p2 = 6.5 p2 = 1.5 M
 Projections p1 = 1 m and p2 = 1.5 m
3. Shear force and Bending Moment Diagram: (SFD & BMD):
Net Upward Pressure / m2 q =
𝑂𝑛𝑙𝑦 𝐶𝑜𝑙𝑢𝑚𝑛 𝑙𝑜𝑎𝑑
𝑎𝑟𝑒𝑎 𝑜𝑓 𝑓𝑜𝑜𝑡𝑖𝑛𝑔
=
2850
6.5∗2.5
Net Upward Pressure/ m
o
q = 175.4 KN/m2
q = q x B

## Slide 8
= 175.4 * 2.5
= 438.5KN/m

## Slide 9
Shear Force Calculation:
SF at A = 0
SF up to B SF at B SF up to C Sf at C
= + 438.5 * 1 = 438.46 KN
= + 438.5 – 1250 = - 811.54 KN
= - 438.5 *1.5 = - 657.7 KN
= - 657.7 + 1600 = + 942.3 KN
SF at D = 0
Bending Moment Calculation:
BM at A | = 0 | 
BM at B | = | + 438.46 * 1 *1/2 = + 219.23 KN-m
BM at O | = | + 438.46*2.85*2.85/2 -1250*1.85 = - 531.80 KN-m
BM at C | = | + 438.46*5*5/2 – 1250*4 = + 480.75 KN-m
BM at D | = | 0
Location of Zero Shear Force:
The point where SF=0, the BM is maximum
From Shear force diagram, from two similar triangles, we can write
=
811.54 942.3
𝑥 (4−𝑥)
 x = 1.85 m
i.e Shear force is zero at a distance of 1.85 m from B.

## Slide 10
Location of POC’s:
POC is the point where BM changes its sign Therefore equating BM at x-x = 0
438.46 * x *x /2 – 800 (x-1) = 0
219.23 *x2 -1250* x + 1250 = 0
Solving Quadratic equation, x1 = 4.10 m & x2 = 1.5 m
4. Design of Slab:
Provide width of Beam is equal to size of bigger column
 Beam width = 600 mm

## Slide 11
Taking moment about Critical Section x - x
2
 M = 175.4*0.95* 0.95 = 79.15 KN-m
Mu = 1.5 *M = 1.5 *79.15 = 118.72 KN-m
Thickness or Depth of Slab: Equating Mu to Mulimit
u
M = 0.36
𝑢,𝑚𝑎𝑥
𝑥 𝑥
𝑢,𝑚𝑎𝑥
𝑑 𝑑
𝑐𝑘
[1 − 0.42 ] 𝑓 𝑏 𝑑2
118.72 * 106 = 0.36 ∗ 0.48[1 − 0.42 ∗ 0.48] ∗ 20 ∗ 1000 ∗ 𝑑2
d = 207.4 mm
Using 60 mm effective cover
Overall depth D = 207.4 + 60 = 267 mm say 270 mm

## Slide 12
But from shear consideration, double the above thickness
 D = 540 mm and d = 480 mm
Area of Steel:
Mu = 0.87 fy Ast d[1 −
Ast fy
fck b d
]
118.72 x 106 = 0.87 ∗ 415 ∗ Ast ∗ 480[1 −
Ast∗415
20∗1000∗480
]
Ast = 706.62 mm2
Providing 12 mm dia bars, Spacing is taken least of the following
𝜋 ∗ 122
4
𝐴𝑠𝑡 706.62
i. Spacing = 𝑎𝑠𝑡 * 1000 = ∗ 1000 = 160 mm ii.
iii.
Spacing = 3d = 3 * 480 = 1440 mm Spacing = 300 mm
 Provide 12mm dia bars @ 160mm c/c
Distribution Steel:
100
0.12
Ast = 0.12 % of Gross Area = * 1000 * 540 = 648 mm2
Providing 10 mm dia bar, Spacing is taken as least of the following
𝜋∗ 102
4
𝐴𝑠𝑡 660
∗ 1000 = 121 𝑚𝑚 ≈ 120 𝑚𝑚
i. Spacing = 𝑎𝑠𝑡 * 1000 = ii.
iii.
Spacing = 5d = 5 * 480 = 2400 mm Spacing = 450 mm
 Provide 10mm dia bars @ 110 mm c/c

## Slide 13
5. Design of Beams:
Beam Width b = 600 mm
AB and CD portion are designed as Rectangular Beam and BC portion is designed as T – Beam.

## Slide 14
Concrete is very weak in tension, hence neglect the concrete portion in tension zone.
Mmax = 531.8 KN-m (From BM Diagram) Mu = 1.5 * 531.8 = 797.7 KN-m
Equating Mu to Mulimit
u
M = 0.36
𝑥 𝑥
𝑢,𝑚𝑎𝑥 𝑢,𝑚𝑎𝑥
𝑑 𝑑
𝑐𝑘
[1 − 0.42 ] 𝑓 𝑏 𝑑2
797.7 * 106 = 0.36 ∗ 0.48[1 − 0.42 ∗ 0.48] ∗ 20 ∗ 600 ∗ 𝑑2
d = 694.14 say 700 mm
 Beam dimensions b = 600 mm, d = 700 mm and D = 760mm
(i) Design of “AB”Portion:
MAB = 219.23 KN-m. (From BM diagaram) Mu = 1.5 * 219.23 = 328.84 KN-m
In AB portion, tension is in the flange, hence neglecting tension zone, Take b = 600mm
Area of Steel:
Mu = 0.87 fy Ast d[1 −
Ast fy
fck b d
]
328.8 x 106 = 0.87 ∗ 415 ∗ Ast ∗ 700[1 −
Ast∗415
20∗600∗700
]
Ast = 1397.6 mm2
Providing 20 mm dia bars,

## Slide 15
𝐴𝑠𝑡
No. of bars = =
𝑎𝑠𝑡
1397.6
3.14∗ 202
4
= 5 bars.
(ii) Design of “CD”Portion:
MCD = 480.75 KN-m. (From BM diagram) Mu = 1.5 * 480.75 = 721.12 KN-m
Even in CD portion, tension is in the flange, hence neglecting tension zone, Take b = 600mm
Area of Steel:
Mu = 0.87 fy Ast d[1 −
Ast fy
fck b d
]
721.12 x 106 = 0.87 ∗ 415 ∗ Ast ∗ 700[1 −
Ast∗415
20∗600∗700
]
Ast = 3437 mm2 Providing 25mm dia bars,
No. of bars = =
𝑎𝑠𝑡
𝐴𝑠𝑡 1397.6
3.14∗ 252
4
= 7 bars.
(iii) Design of “BC”Portion:
MBC = 531.8 KN-m. (from BM diagram) Mu = 1.5 * 531.8 = 797.7 KN-m
In this portion, tension is in WEB, hence neglecting, web portion and considering flange
 b = bf = effective flange width
Hence beam is designed like a T- Beam

## Slide 16
For Isolated T-Beam
f
Effective flange width b =
𝑙𝑜
𝑙𝑜
( 𝑏 )+4
𝑤
+ 𝑏 ----Page 37, IS 456
b = Actual flange Width = 2500
𝑙𝑜 = Distance between points of zero moments
𝑙𝑜 = Distance between POC
= (x1 - x2) = 4.4 - 1.29 = 3.11 m = 3110 mm
From BMD
Therefore,
bf =
3110
3110
2500
( )+4
+ 600 = 1193 mm
Area of Steel:
Mu = 0.87 fy Ast d[1 −
Ast fy
fck 𝑏𝑓 d
]
797.7 x 106 = 0.87 ∗ 415 ∗ Ast ∗ 700[1 −
Ast∗415
20∗1193∗700
]
Ast = 3453.5 mm2

## Slide 17
Providing 25mm dia bars,
𝐴𝑠𝑡
No. of bars = =
𝑎𝑠𝑡
3453.5
3.14∗ 252
4
= 7 bars.
Design of Beam for Shear:
Maximum shear force Vmax = 942.3 KN (From SFD )
Ultimate shear force = 1.5 * 942.3 = 1413.4 KN b = 600mm, d = 700 mm, Ast = 3453.5 mm2
Nominal Shear force τv =
=
𝑉𝑢 1413.4∗103
𝐵 𝑑 600∗700
= 3.36 N/mm
2
Shear Stress in Concrete:( τc )
Pt =
100 𝐴𝑠𝑡
𝑏 𝑑
=
100 ∗3453.5
600∗700
= 0.82
Referring to IS 456, Pg 73, for Pt = 0.82 and M20 Concrete
 τc = 0.58 N/mm2
Comparing
τv and τc ,
τv > τc
,  Provide Shear Reinforcement
Vertical Stirrups:
Using 4L - #10 mm Vertical stirrups
sv
4
𝜋∗ 102
A = 4 * = 314.16 mm2
Shear force to be carried by vertical stirrups

## Slide 18
Vus = (Vu - τc * b*D) = (1413.4 * 103 -0.58*600*700)
= 1169.83 kN
From IS 456, Page 73
Vus =
0.87 𝑓𝑦 𝐴𝑠𝑣 𝑑
𝑆𝑣
 Spacing of Vertical Stirrups from above equation
Sv =
0.87 𝑓𝑦 𝐴𝑠𝑣 𝑑
𝑉𝑢𝑠 0.87∗415∗314.15∗700
Sv =
1169.83∗103
= 67.87 mm say 65 mm
Provide 4L – #10 mm Vertical Stirrups @ 65 mm c/c below the Column and @ 300 mm c/c in other places
o
Shear strength of Concrete at distance x from apex (from o) of above triangle
Vc = τc *b*d = 0.58 *600*700
= 243.6 KN

## Slide 19
Distance x from above similar triangles
1413.4 = 243.6
2.15 𝑥

 x = 0.37 m.
Spacing of Stirrups:
Vertical Stirrups @ 65 mm c/c below the Column and @ 300 mm c/c in other places (0.37m from apex of the triangles)
Plan showing Slab, Beam and Column

## Slide 20
Plan showing reinforcement in slab
Cross Section at Mid span
(X2 – X2)

## Slide 21
Cross Section through the Column (X3 – X3)
Longitudinal Cross Section (X1 –X2)

## Slide 22
Ld = 47Ф for M25
Longitudinal Section showing reinforcement in beam

## Slide 23
DESIGN OF WATER TANKS
(Working stress method using IS 3370 – Code of Practice for Concrete structure for the storage of liquids)
Following are the different types of water tanks to be designed
Design of circular water tank with rigid base.
Design of circular water tank with flexible base.
Design of rectangular water tank.
Working Stress Method:
a. Permissible Stresses in Concrete:
σcbc = Permissible Bending Compressive Stress in concrete.
σct = Permissible Tensile Stress in Concrete.
Grade of Concrete | σcbc | σct
M15 | 5 N/mm2 | 1.10 N/mm2
M20 | 7 N/mm2 | 1.20 N/mm2
M25 | 8.5 N/mm2 | 1.30 N/mm2
b. Permissible Tensile Stresses in Steel:
σst = Permissible Tensile stress in Steel.
Grade of Steel | Near Water face | Away from Water face
Mild steel or Fe 250 | 115 N/mm2 | 125 N/mm2
HYSD or Fe 415 or Fe 500 | 150 N/mm2 | 190 N/mm2

## Slide 24
280
3𝜎𝑐𝑏𝑐
c. Working Stress Constants:
Modular ratio m =
Neutral axis c0efficient k =
Lever arm constant
𝑚 𝜎𝑐𝑏𝑐
𝑚 𝜎𝑐𝑏𝑐+ 𝜎𝑠𝑡
j = 1 -
𝑘 3
iv. Moment of Resistance coefficient
𝜎𝑐𝑏𝑐 𝑘 𝑗
Q =
2
𝑀
𝑄 𝑥 𝑏
Effective depth d = √
Area of Steel
If the moment is known Ast =
𝑀
𝜎𝑐𝑏𝑐 𝑗 𝑑
If force is known Ast =
𝐹𝑜𝑟𝑐𝑒
𝜎𝑠𝑡
d. Specifications for the design of Water Tank:
Adopt clear cover = 30 mm
Minimum reinforcement
Up to 100mm thick wall = 0.3% of Gross Area Between 100 & 450 mm thick wall = 0.2% of Gross Area
Thickness of wall (T)
  T = 30 H + 50 mm, Where H = Depth of water in m
2.
σcbc =
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝐻𝑜𝑜𝑝 𝑇𝑒𝑛𝑠𝑖𝑜𝑛
1000 𝑇+(𝑚−1)𝐴𝑠𝑡.
iv. w = Unit weight of water = 1000 N/m3
= 1 KN/m3
Also 1000 lts = 1 m3
 1 lt = 1 * 10-3 m3

## Slide 25
Design of circular water tank with flexible Base.
Design a circular water tank with flexible base for a capacity of 4 x 105 lts. The depth of water tank is to be 4m with a free board of 200 mm. Use M25 and Fe 415 steel.
Draw the following sketches
  Cross section of the tank
  Half plan through the wall
  Half plan through the base slab. Data given:
Capacity = 4 x 105 lts. Depth H = 4m
Free board = 0.2 m
Take Unit weight of water = 9.81 KN/m3
= 981 N/m3

## Slide 26
1. Design Constants
For M25, σcbc = 8.5 N/mm2 , σct = 1.31 N/mm2
For Fe 415,
σst = 150 N/mm2
280
3𝜎𝑐𝑏𝑐
Modular ratio m = =
280
3∗8.5
= 10.98
2. Dimensions of the Water Tank:
Equating capacity to volume
i.e. capacity = Volume
4 x 105 lts. = Area * Height
m3=
4 x 105 𝜋
1000 4
𝐷2
* 4 m
D = 11.28m say D = 11.3 m.
3. Hoop Tension ( in the bottom 1m height) Here H = 4 m from top
Maximum Hoop tension = W *H *
𝐷 2
= 9.81 * 4 *
11.3
2
= 221.70 KN
 Area of hoop tension steel, A
st
𝐹𝑜𝑟𝑐𝑒 𝑚𝑎𝑥.𝐻𝑜𝑜𝑝 𝑡𝑒𝑛𝑠𝑖𝑜𝑛
= σst = σst
150
221.70∗ 103
Ast = = 1478 mm2
Providing 16 mm dia bars
Spacing =
𝑎𝑠𝑡
𝐴𝑠𝑡
𝜋∗ 162
1478
∗ 1000 = 4 ∗ 1000 = 136.03 = 130 mm
 Provide #16mm hoop tension steel @ 130 mm c/c in the bottom 1m height

## Slide 27
4. Hoop Tension in 1m to 2 m from bottom: Here H = 3 m from top
Hoop tension = W *H1 *
𝐷 2
= 9.81 * 3 *
11.3
2
= 166.27 KN
 Area of hoop tension steel, A
st
𝐹𝑜𝑟𝑐𝑒 𝐻𝑜𝑜𝑝 𝑡𝑒𝑛𝑠𝑖𝑜𝑛
= σst = σst
150
166.27∗ 103
Ast = = 1108.46 mm2
Providing 16 mm dia bars
Spacing =
𝑎𝑠𝑡
𝐴𝑠𝑡
𝜋∗ 162
1108.46
∗ 1000 = 4 ∗ 1000 = 181.3 = 180 mm
 Provide #16mm hoop tension steel @ 180 mm c/c between 1m to 2m from
bottom
5. Hoop Tension between 2m – 3m from bottom: Here H = 2 m from top
Hoop tension = W *H2 *
𝐷 2
= 9.81 * 2 *
11.3
2
= 110.85 KN
 Area of hoop tension steel, A
st
𝐹𝑜𝑟𝑐𝑒 𝐻𝑜𝑜𝑝 𝑡𝑒𝑛𝑠𝑖𝑜𝑛
= σst = σst
150
110.85 ∗ 103
Ast = = 739 mm2
Providing 16 mm dia bars

## Slide 28
Spacing =
𝑎𝑠𝑡
𝐴𝑠𝑡
𝜋∗ 162
739
∗ 1000 = 4 ∗ 1000 = 270 mm
 Provide #16mm hoop tension steel @ 270 mm c/c between 2m to 3m from
bottom
Wall Thickness: (T)
  T = 30 H + 50 mm, Where H = Depth of water in m
= 30 * 4 + 50 mm = 170 mm
2.
σcbc =
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝐻𝑜𝑜𝑝 𝑇𝑒𝑛𝑠𝑖𝑜𝑛
1000 𝑇+(𝑚−1)𝐴𝑠𝑡.
221.70 ∗ 103
1.30 = 1000 𝑇 + (10.98 − 1) ∗ 1478
T = 155.78 mm
 Take T = 170 mm
7. Steel for remaining top 1 m height: (between 3 to 4 m) For top 1m, provide minimum steel,
For 100 thick wall, Minimum steel For 450 thick wall, Minimum steel
= 0.3 % of gross area
= 0.2 % of gross area

## Slide 29
 Provide #12 mm hoop tension steel @ 230mm c/c from top 1m
 Provide #10 mm @ 160 mm c/c as Vertical Steel.
 For 170 thick wall, Minimum steel
= 0.28 % of gross area
= 0.28/100 * (1000 *170)
= 476 mm2
Using 12 mm dia bars
Spacing =
𝑎𝑠𝑡
𝐴𝑠𝑡
𝜋∗ 122
476
∗ 1000 = 4 ∗ 1000 = 237 say 230 mm
7. Vertical Distribution Steel:
Area of steel
= 0.28 % of gross area
= 0.28/100 * (1000 *170)
= 476 mm2
Using 10 mm dia bars
Spacing =
𝑎𝑠𝑡
𝐴𝑠𝑡
𝜋∗ 102
476
∗ 1000 = 4 ∗ 1000 = 164 say 160 mm
8. Base slab Design (Floor slab):
Base slab is continuously supported on ground, therefore provide a minimum thickness of 150 mm and reinforcement of 0.3 % of steel in the form of mesh @ top and bottom
 Area of steel =
=
=
0.3% of Area 0.3/100 *(1000*150)
450 mm2
Using 10 mm dia bars

## Slide 30
 Provide #10 mm @ 170 mm c/c
Spacing =
𝑎𝑠𝑡
𝐴𝑠𝑡
𝜋∗ 102
450
∗ 1000 = 4 ∗ 1000 = 174.53 say 170 mm

## Slide 32
Design of Circular Water Tank with RIGID BASE
(Fixed or rigid base or restrained at the base)
Design a circular water tank of an internal dia 10 m and height 4m, the walls are restrained at the base. Use IS code method. Design the tank for M25 and Fe415. Draw sketches showing reinforcements
  Cross section of water tank.
  Draw half plan through wall.
  Draw half plan through base slab.
Given Data:
Diameter = 10m, height = 4m, Assume free board = 0.2 m
1. Design Constants:
For M25, σcbc = 8.5 N/mm2 , σct = 1.31 N/mm2
For Fe 415,
σst = 150 N/mm2
m =
3𝜎𝑐𝑏𝑐
280 280
3∗8.5
= = 10.9
k =
𝑚 𝜎𝑐𝑏𝑐
𝑚 𝜎𝑐𝑏𝑐+ 𝜎𝑠𝑡
=
10.98∗ 8.5
10.98∗8.5 + 150
= 0.383
j = 1 -
0.383
3
= 0.872
1

## Slide 33
Q =
8.5∗0.383∗0.872
2
= 1.42
Thickness of Wall:
T = 30 H + 50 mm = 30*4 +50 = 170 mm
Using 50 mm Effective Cover, d = 170 – 50 = 120 mm
Hoop Tension and Bending Moment (Ring Tension): Hoop Tension:
From IS 3370 (Part IV) , Table-9, Page 35
Hoop Tension = Coefficient * H * 𝐷/2 *W (Kg/m)
Ratio = =
𝐻2 42
𝐷𝑇 10∗170
= 9.41
Search for the maximum values, it coincides at 0.6 H
For 8 – 0.578
10 – 0.602
By interpolating for 9.41 – 0.598 ≈ 0.6
 Hoop Tension = 0.6 *4 * 10/2 * 9.81 = 117.72 KN Bending Moment:
From IS 3370, Table 10, page 36
Moment = Coefficient * W *H3
Ratio = =
𝐻2 42
𝐷𝑇 10∗170
= 9.41
2
Search for the maximum values, it coincides at 1.0 H

## Slide 34
For 8 – 0.0146
By interpolating
10 – 0.0122
for 9.41 – 0.0129
Ast =
𝑀 8.10 ∗ 106
𝜎𝑠𝑡∗𝑗∗𝑑 150∗0.872∗135
= = 459 mm2
T = 170 mm, Using 10 mm bar and 30 mm clear cover d = 170 – 30 – 10/2 = 135 mm
Check for minimum Steel
Min Steel = 0.3 % of Gross area, for T = 100 mm
= 0.2 % of Gross area, for T = 450 mm For T = 170 mm Min Steel = 0.28 % of Gross area
 Moment = Coefficient * W *H3 = 0.0129*9.81*43
= 8.10 KN-m
Area of Steel:
a. Hoop Steel for Hoop Tension:
3
Ast = 𝐻𝑜𝑜𝑝 𝑇𝑒𝑛𝑠𝑖𝑜𝑛 = 118∗10 = 786.67 mm2
𝜎𝑠𝑡 150
Providing 12 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗12 /4 * 1000 = 140 mm
𝐴𝑠𝑡 786.67
 Provide 12mm dia bars @ 140 mm c/c up to a depth = 0.6 H =
2.4 m from bottom and 280 mm c/c for the remaining depth
b. Bending Moment or Cantilever Steel:
3

## Slide 35
 Ast = 0.28/100 * 1000 * 170 = 476 mm2
Providing 10 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗10 /4 * 1000 = 160 mm
𝐴𝑠𝑡 476
 Provide 10mm dia bars @ 160 mm as Cantilever steel up to a height of 0.4*H = 1.6m ( or 4 – 2.4 = 1.6 m) from bottom
c. Vertical Distribution Steel:
Area of steel = 0.28 % of Gross Area
 Ast = 0.28/100 * 1000 * 170 = 476 mm2
Providing 8 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗8 /4 * 1000 = 100 mm
𝐴𝑠𝑡 476
 Provide 8 mm dia bars @ 100 mm
5. Base Slab Design:
Provide 150 mm thick slab with 0.3% of Gross area of steel in the form of mesh @ top and bottom.
Area of steel = 0.3 % of Gross Area
 Ast = 0.23/100 * 1000 * 150 = 450 mm2
Providing 10 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗8 /4 * 1000 = 170 mm
𝐴𝑠𝑡 476
 Provide 10 mm dia bars @ 170 mm c/c in the form of mesh
4

## Slide 36
Cross Section of Water Tank (fixed)
Also provide haunch 150 mm x 150 mm with 8mm dia bars @ 200 mm c/c
5

## Slide 37
6

## Slide 38
7
Design a circular water tank 12 m dia, 4 m height, the tank rests on ground, the wall is fixed on a base slab. Use M20 concrete and Fe 415 steel. Adopt working stress method and design as per 3370. Also draw the following sketch
  Section through the tank.
  Base slab reinforcement at top and bottom.

## Slide 39
Page1
Design of Rectangular Water Tank ( By using IS 3370 –Part(4)
1. A rectangular water tank with an open top is required to store 80,000 lts of water. The inside dimension of the tank may be taken as 6 x 4 m. Design the side wall of the tank using M20 Concrete and Fe415 steel. Use IS method. Also draw
Sectional plan of the tank Longitudinal section of the tank Cross Section of the tank.
a.
b.
c.
Given Data:
Capacity = 80,000 lts
Inside dimension L = 6m, B = 4m
1. Design Constants:
For M20 For Fe415
𝜎𝑐𝑏𝑐 =
7 N/mm2 𝜎𝑐𝑡 = 1.2 N/mm2
𝜎𝑠𝑡
= 150 N/mm2
i. Modular ratio
m =
280
3𝜎𝑐𝑏𝑐
=
280
3∗7
= 13.33
ii. Neutral axis coefficient k =
𝑚 𝜎𝑐𝑏𝑐
𝑚 𝜎𝑐𝑏𝑐+ 𝜎𝑠𝑡
=
13.33∗7
(13.33∗7+ 150
= 0.383
iii.
0.383
3
Lever arm constant j = 1 -
iv. Moment of Resistance coefficient Q =
= 0.8723
7∗ 0.38∗0.87
2
= 1.16

## Slide 40
Page2
Equating Capacity to volume
i.e. Capacity = Volume 80,000 lts = Area * Height
80 m3 = L * B * H
80 = 6 * 4 * H H = 3.33 m
Providing 0.17 m as free board, H = 3.33 + 0.17 = 3.5 m
Moment Calculation:
  Moment Calculation for long wall: As per IS 3370, table 3,
Horizontal moment Vertical moment
= My w a3
= Mx w a3
a = height of the wall
= 3.5 m
H = 3.5 m
L = 6 m
B=4 m
Short wall
Long wall Corner
Long Wall
Free board

## Slide 41
Page3
b = Width of wall
 Ratio = b/a = 6/3.5 = 1.71
= 6 m
My
Mx For 1.75 …………… 0.074
For 1.71 ?
For 1.5 …………… 0.060
0.052
?
0.044
 By interpolating for 1.71 Mx = 0.0719 & My = 0.051
 Horizontal moment = 0.051 * 10 * 3.53 = 21.86 KN-m
 Vertical moment = 0.071 * 10 * 3.53 = 30.87 KN-m
ii)
Moment calculation for short Wall: a = height = 3.5 m, b = 4 m Ratio b/a = 4/3.5 = 1.14
My
Mx For 1.25 …………… 0.047
For 1.14 ?
For 1.0 …………… 0.035
0.037
?
0.029
 By interpolating for
 Horizontal moment
 Vertical moment
1.14, Mx = 0.042 & My = 0.033
= 0.033 * 10 * 3.53 = 14.14 KN-m
= 0.042 * 10 * 3.53 = 18 KN-m
Select the Max Coefficients
Select the Max coefficients

## Slide 42
Page4
iii)
Moment for long wall Corner:
a = height = 3.5 m, b = 6 m Ratio = b/a = 6/3.5 = 1.71 Also y = b/2
From IS 3370, table 3,
 | Mx | My
For 1.75 …………… | 0.01 | 0.052
For 1.71 | ? | ?
For 1.5 …………… | 0.009 | 0.044
 By interpolating for 1.71, Mx = 0.009 & My = 0.050 Neglect Mx value since coefficient is very small
Horizontal moment = My w a3 = 0.050 * 10 * 3.53 = 21.437 KN-m
Select the Max coefficients

## Slide 43
Page5
3. Tank wall thickness:
Maximum Bending moment = 30.87 KN-m
 Effective depth d = √ 𝑚
𝑄∗𝑏 1.16∗1000
= √30.87∗ 106
= 163.12 mm
Providing 50mm effective cover D= 63.13 + 50 = 213.13 ≈ 220 mm
 Provide D = 220 mm & d = 170 mm
Pull in each Wall:
Pull in long wall = 𝑤𝐻𝐵 = 10∗3.5∗4 = 70 KN
2 2
Pull in short wall = 𝑤𝐻𝐿 = 10∗3.5∗6 = 105 KN
2 2
Design of long wall:
50
X
d = 170
220
2
220
X = (170 - )
= 60 mm

## Slide 44
Page6
i. Hoop steel or Horizontal Steel:
Ast =
𝑀−𝑇.𝑥 + 𝑇
𝜎𝑠𝑡 .𝑗.𝑑 𝜎𝑠𝑡
where M = Horizonal Moment = 21.86 KN-m,T = 70 KN
9 3 3
Ast = 21.86∗ 10 (70∗10 ) + 70∗10
150∗0.87∗170 150
Providing 16 mm dia bars,
= 1263 mm2
ii. Vertical Steel
Ast =
𝑀
𝜎𝑠𝑡 .𝑗.𝑑
Ast =
30.87∗ 109
150∗0.87∗170
= 1392 mm2
Ast =
𝑀−𝑇.𝑥 + 𝑇
𝜎𝑠𝑡 .𝑗.𝑑 𝜎𝑠𝑡
where M = Horizonal Moment = 14.14 KN-m, T = 105 KN
6 3 3
Ast = 14.14∗ 10 (105∗10 ) + 105∗10
150∗0.87∗170 150
= 1054 mm2
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗16 /4 * 1000 = 160 mm
𝐴𝑠𝑡 1263
 Provide 16 mm dia bars @ 160 mm c/c
Providing 12 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗12 /4 * 1000 = 81.24 mm say 80 mm
𝐴𝑠𝑡 1392
 Provide 12 mm dia bars @ 80 mm c/c
6. Design of Short Wall:
i. Hoop steel or Horizontal Steel:

## Slide 45
Page7
ii. Vertical Steel:
Ast =
𝑀
𝜎𝑠𝑡 .𝑗.𝑑
Ast =
18∗ 106
150∗0.87∗170
= 811.35 mm2
Ast =
𝑀
𝜎𝑠𝑡 .𝑗.𝑑
Ast =
21.43∗ 106
150∗0.87∗170
= 966 mm2
Providing 16 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗16 /4 * 1000 = 190 mm
𝐴𝑠𝑡 1054
 Provide 16 mm dia bars @ 190 mm c/c
Providing 12 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗12 /4 * 1000 = 139.2 mm say 140 mm
𝐴𝑠𝑡 811.35
 Provide 12 mm dia bars @ 140 mm c/c
7. Design of Corner Wall :
Providing 16 mm dia bars,
2
Spacing = 𝑎𝑠𝑡 * 1000=π∗16 /4 * 1000 = 200 mm
𝐴𝑠𝑡 966
 Provide 16 mm dia bars @ 200 mm c/c

## Slide 46
Page8
8. Design of Base Slab:
Provide minimum thickness = 150 mm
Also provide minimum steel in the form of mesh at the top and bottom = #10 @150 mm c/c.
Sectional Plan of the tank

## Slide 47
Page9

## Slide 48
Page10
A rectangular water tank with an open top is required to store 1,00,000 lts of water. The inside dimension of the water tank may be taken as 8 m x 4m. The tank rests on ground. Design the side walls of the tank using the following
Permissible Compressive stress in concrete = 7 N/mm2 Permissible Tensile stress in steel = 150 N/mm2 Modular ratio = 13.33
Draw the following sketches.
  Sectional elevation through short wall.
  Sectional elevation through long wall.
  Sectional plan. Solution:
Following are steps in the design
    Design Constants and height of the tank
    Moment Calculation
      Moment calculation for long wall
      Moment calculation for short wall
      Moment calculation for long wall corner.
    Tank wall Thickness
    Pull in each wall
    Design of long wall
    Design of short wall
    Design of corner wall
    Design of base slab
Design side walls of rectangular reinforced water tank of dimensions 6m x 2 m having a maximum depth of 2.5m using M20 grade concrete and Fe 415 HYSD bars.
Draw a sketch of
  Sectional plan of the tank
  Longitudinal section of tank
  Cross section of the tank.

## Slide 49: HINGED PORTAL FRAME

## Slide 51
HINGED PORTAL FRAMES
Problem
An RCC portal frame with a hinge base is required to suit the following data Spacing of portal frames = 4m c/c
Height of columns = 4m
Distance between column centres=10m Live load on the roof = 1.5kN/m2
The RC slab is continuous over portal frames SBC of soil = 200kN/m2
Materials M20 and Fe 415 steel.
Design the slab, portal frame and foundations. Draw to a suitable scale
i)
Sectional elevation of half frame showing the details of reinforcement in footing, column and beam of portal frame.
Transverse section of beam and column
Sectional plan of footing and column
Design:-
Design of continous slab
Effective depth = = = 153.85mm
Assume 0.3% tension reinforcement, modification factor 1.4 Hence effective depth = = 109.9mm
Assume a clear cover of 20mm and 10mm diameter bars. Total depth = 109.9+20+ = 134.9mm say 150mm

## Slide 52
Dead load on the slab = 0.15X24 = 3.6kN/m2
Roof finishes = 0.756kN/m2
Ceiling finishes = 0.256kN/m2 Dead load/m2 g = 4.6kN/m2
Live load/m2 q = 1.5kN/m2
Maximum Negative BM
M = +
M = 4.6 x + 1.5 x M = 10.03kN-m
Maximum Positive BM
M = +
M = 4.6 x + 1.5 x M = 8.53kN-m
Factored design moment = 1.5x10.03=15kN-m Assuming an effective depth as 0.9 times the total depth,
Ultimate resisting moment = = 50.3kN-m>15kN-m, Hence ok. Effective depth provided = 150-20-(10/2) =125mm
Design of reinforcement at top and bottom:-
15x106=0.87x415xAstx125 (1 - )

## Slide 53
1.66x10-4Ast2-Ast +332.36=0
Ast=353mm2
Spacing of #10 = *1000= 222.5mm
Use #10 @ 200mmc/c
Distribution Steel:-
Ast== x 1000x150 = 180mm2
Spacing of #8 = *1000= 279mm
Use #8 @ 250mmc/c
Design of Portal Frame
Effective span of beam = 10m
Effective depth of the beam =
to
= 833.33mm to 666.7mm
Effective depth = 700mm
Overall depth= 750mm Width of beam = 450mm
Load on frame
Load from the slab = (4.6+1.5)x4x1 = 24.4kN/m Self-weight of beam = 0.45x0.63x1x25 = 7.1kN/m Self-weight of finishes = 0.5kN/m
Load/m = 32kN/m
Height of centre line of beam above hinge, h = (4+0.10-0.5x0.75) = 3.72 m

## Slide 54
0.67 | 0.33
AB BA | BC
+177.8 | -266.7 +88.9
0 +177.8 | -177.8
AB = 3.72m;
BC = 10m
IAB =
= 8.1x109mm4
IBC = = 1.58x1010mm4
IAB : IBC = 1:1.95
Relative stiffness values
KBA =( x ) = 0.2I
0.3I
KBC = ( ) = 0.1I
dBA = 0.2/0.3 = 0.67 dBC = 0.1/0.3 = 0.33
Fixed End Moments
Fig - 1
MFBC =
= -266.7 kNm
MFCB =
= +266.7kNm
Design Moments and Shear force
Maximum Negative BM = 177.8 kN-m
Maximum positive moment at centre of span =
177.8 = 222.2kN-m

## Slide 55
Maximum shear force at B =
= 160kN
Shear force at the hinge at A = = 47.8kN
Factored moment at support B = 1.5x177.8=266.7kNm Factored moment at centre of span= 1.5x222.2=333.3kNm Factored shear force at hinge at A = 1.5x47.8 = 71.7 kN Factored shear force at support B = 1.5x160=240kN DESIGN OF BEAMS
Central section:-
Assume dimensions of the beam are
bw = 450mm, d = 700mm, Df = 150mm
bf= +bw +6Df = +450+(6*150)= 3017mm
=
= 0.011
= 0.36 )(1-0.42x ) = 0.07
hence NA is inside the flange.
Fig-2
333.3x106=0.87x415xAstx700
Ast = 1336.3mm2
Use 4# of 25mm dia bars
Support section:-
Mu =266.7kN-m 266.67x106=0.87x415xAstx700

## Slide 56
Ast= 1141mm2
Use 4# of 20mm dia bars
DESIGN OF SHEAR REINFORCEMENT:-
Vu = 240kN
=
= 0.76N/mm2
=
= 0.62
Interpolation
0.50 0.48
0.62 ? 0.75 0.56
=0.52N/mm2
Vus=240x103-(0.52x450x700) =76200
76200 = 0.87x415x2x
*700
SV =333mm
Use 2L #8 @ 300c/c
Design of Column
Mu = 266.7 kN-m Vu = 240kN

## Slide 57
=
= 0.082
= = 0.044
Referring to the chart given in SP16
= 0.04
P=0.04x20=0.8
Ast= = 0.8x450x = 2160 mm2
Use 4#20 and #8 @ 300 as ties
DESIGN OF HINGE:-
Permissible bearing stress at the hinge = 0.5fck=10N/mm2
Area of hinge = =16000mm2
Area provided = 450*150 16000mm2 Working shear at the hinge = 47.8kN Factored shear at the hinge = 71.7kN Asvsin45x0.87x415 = 71.7x103
Asv = 280.9mm2
Use 4# 12mm dia
Spiral consisting of 10mm dia with 6mm diameter
Design of foundation
Axial load on the column
= 160kN
Weight of column = 0.45 x 0.6x 3.72x 24
= 24kN

## Slide 58
Self-weight of foundation 10%
= 16kN
Total load
= 200kN
= 47.8 kN-m
Moment about the base (M) =47.8*1
Eccentricity e = = =0.239m Breadth of foundation = 6X239=1434mm
Provide a foundation of 1mX2m
Intensity of maximum pressure =
= 150kN/m2 < 200kN/m2
p
X150=97.5 kN/m2
Total pressure on cantilever portion =
= 86.6 kN
BM, Mu= (86.6*
=45kN-m
Effective depth required =
= 127.6mm
From the shear considerations; double the effective depth say D= 300mm
Design of main reinforcement
45X106=0.87X415XAstX250 (1-
X )
Ast=521mm2
Spacing of #12 =
*1000= 217mm
Use #12 @ 200mm c/c in both ways
Distribution steel, Ast== x 1000x300 = 360mm2

## Slide 59
Spacing of #10 =
*1000= 218mm
Use #10 @ 200mm c/c

## Slide 60
Module 2
Design of Steel Structures Design of Roof Trusses:
Following points are followed while designing the roof truss
Select double angle for top chord and bottom chord members and single angle for inner members.
Provide minimum two number of bolts for the connection in Bolted roof truss.
Take effective length ι e = 0.85 ι
Provide uniform thickness of gusset plate
Select minimum size of angle i.e. ISA 50 x 50 x 6 mm
Design only four member’s i.e.
  Outer Maximum Compression Member
  Outer Maximum Tension Member
  Inner maximum compression member
  Inner maximum tension member
1 | P a g e

## Slide 61
The Centre line diagram of the steel truss is shown in figure. The magnitude and nature of forces in different members of the truss are given in table. The size of the RC column supporting the truss is 300 x 300 mm. Use M20 concrete for Column.
Design the truss using bolted or welded connection. Also design anchor bolts for an uplift force of 15 KN at each support.
Draw rough sketches of following
  Elevation of truss greater than half span.
  Enlarged view of apex joint of the truss.
  Enlarged view of the left support joint.
D
Member | Force (KN) | Length (m)
AC,EB | -80 KN | 3.46
CD,DE | -70 KN | 3.46
AF,GB | +70 KN | 4
FG | +50 KN | 4
CF,EG | -24 KN | 2
DF,DG | +24 KN | 4
Reaction, Ra = Rb = 50 KN
-ve = Compession, +ve = Tension
C
A
B
2 | P a g e
E
4 M
F
4M G 4M
AC = CD = DE =EB

## Slide 62
Soln:
1. Design of outer Compression Member ( Top Chord Member) The members are AC, CD,DE and EB
Member AC Member CD
80 KN (C)
70 KN (C)
L = 3.46 m L = 3.46 m
Select maximum force = 80 KN
Factored force = 1.5 x 80 = 120 KN Maximum length = 3.48 m
Design the top chord as the compression member using double angle and bolts
i. Selection of Section: Assume fcd = 60 N/mm2
Using
Pd = Ac fcd …………….Page no. 34, IS 800 120 x 10 3 = Ac x 60
Ac = 2000mm2 or 20 cm2
From Steel tables select suitable double angle section.
Let us try 2ISA 70 x 70 x 8mm
 Ac = 2116 mm2
Assume gusset plate thickness = 10 mm
3 | P a g e

## Slide 63
From steel table rxx = 21.2mm
ryy = 32.9mm ( For 10 mm gap)
rmin = 21.2 mm
Length of the member L = 3.46 M = 3460 mm
 Effective Length Le = 0.85 L = 0.8 * 3460
= 2941 mm
𝑟𝑚𝑖𝑛
 Slenderness ratio = ƛ = =
𝐿𝑒 2941
21.2
ƛ = 138.72
From table 9C (Page 42 IS 800) For 130 -- fcd = 74.2
For 140 -- fcd = 66.2
 For 138 – fcd = 67.23 N/mm2
 Design Compressive Strength
Pd = Ac * fcd
= 2116 * 67.23
= 142.25 x 103
Hence Safe.
N > 120 KN
ii. Design of Connection:
Using m-16 Bolts and Grade 5.6 black bolts
d = 16 mm, do = 16 + 2 = 18 mm and fu = 500 N/mm2 fu for plate = 410 N/mm2
e = 1.5 * do = 1.5 * 18 = 27 mm say e = 30 mm p = 2.5 *d = 2.5 * 16 = 40 mm
From IS 800, Page 75 Shear strength of Bolt
Vdsb = 
𝑚𝑏
1 𝑓𝑢𝑏
[ (nn Anb +nsAsb) ]
√3
4 | P a g e

## Slide 64
Assume fully threaded bolts and double shear nn = 2 and ns = 0
Vdsb =
1.25 √3
1 500 𝜋 162
4
[ (2* ∗ 0.78 + 0 ) ]
= 72.43 KN
Similarly Bearing Strength
1
V dpb= 
𝑚𝑏
[2.5*kb*d*t*fu) … Page 75 IS 800
kb is taken as least of the following
kb =
𝑒
3𝑑𝑜
𝑝
= 0.55
- 0.25 = 0.49
kb =
3𝑑𝑜
kb
= 𝑓𝑢𝑏
𝑓𝑢
= 1.21
kb = 1
 kb = 0.49
dpb
 V =
1
1.25
[2.5*0.49*16* 8*410) = 51.43 KN or 51.43 x 103 N
 Bolt value = 51.43 KN ( Least of shear and Bearing Strength)
No. of Bolts =
𝐹𝑜𝑟𝑐𝑒
120∗10^3
𝐵𝑜𝑙𝑡 𝑉𝑎𝑙𝑢𝑒 51.43∗10^3
= = 2.3 ≈ 3 Nos
5 | P a g e
Hence adopt 2ISA 70 x 70 x8 mm for top chord.
2. Design of Outer Tension Member (Bottom Chord Member)
The bottom chord members are AF = FG = GB AF = 70 KN (T), L = 4 m
FG = 50 KN (T), L = 4 m GB = 70 KN (T), L = 4 mα

## Slide 65
𝑚𝑙
Maximum force = 70 KN
 Factored force = 1.5 * 70 = 105 KN Maximum Length = 4m
i. Selection of Section:
Using Tdn = 𝛼 𝐴𝑛 𝑓𝑢 ………… Page 33 IS 800
Here Tdn = Factored Load = 105 x 10^3 N
𝑚𝑙
𝛼 = 0.7 𝑎𝑛𝑑  = 1.25
105 x 10^3 = 𝐴𝑛 𝑓𝑢
𝑚𝑙
6 | P a g e

## Slide 74
Force in a members as dead load and live load and also wind load is given below. Take tension as positive and compression as negative. Design the truss and support, given upward reaction at support is equal to 180 KN. Uplift pressure 50 KN. Use M-16 bolt for connection.
Draw the sketches of the following
  Half elevation of the truss
  Enlarged view of apex joint
  Enlarged view of end joint & Intermediate joint.
Member | Dead load (KN) | Live load(KN) | Wind load (KN) | Length (m)
AC | +9.4 | -30 | +50.4 | 3.46
CD | -15.7 | -23.8 | +43.4 | 3.46
CF | -6.93 | -10.4 | +19.9 | 2
DF | +3.74 | +5.64 | -11.4 | 4
AF | +17.35 | +26.4 | -42.8 | 4
FG | +10.39 | +15.8 | -21.5 | 4
1

## Slide 75
Soln:
1. Load Calculation [ DL + LL and DL + WL]
Member | Dead load + Live load (KN) | Dead Load + Wind Load (KN) | Final Design Load (KN) | Length (m)
AC | -20.6 | +59.80 | Top chord +59.80 (T) -39.5(C) | 3.46
CD | -39.5 | +27.7 |  | 
CF | -17.33 | +12.97 | Inner Member -17.33 (C) +12.97 (T) | 4
DF | +9.38 | -7.60 |  | 
AF | +43.75 | -25.45 | Bottom Chord +43.75 (T) -25.45 (C) | 4
FG | +26.19 | -11.11 |  | 
Design of Top Chord Member:
After the load calculation, select the maximum value
Tension force = 59.8 KN , Factored Force = 1.5 * 59.8 = 89.70 KN Compressive Force = 39.5 KN, Factored Force = 1.5 * 39.5 = 59.25 KN Maximum length = L = 3.46 m
 Effective length = Le = 0.85 *3.46 = 2.941 m = 2941 mm
Since tension force is more than compressive force, start the design like a tension member and then check for compressive force.
a. Design of Tension Member:
𝑚𝑙
Using Tdn = 𝛼 𝐴𝑛 𝑓𝑢 …………
Page 33 IS 800
2

## Slide 76
Here Tdn = Factored Load = 89.70 x 10^3 N
𝛼 = 0.6 𝑎𝑛𝑑  = 1.25
𝑚𝑙
89.70 x 10^3 = 0.6∗ 𝐴𝑛∗410
1.25
 An = 455.792 mm2
Increase the area approximately by 30 %
Vdsf Gross area Ag = 1.3 * 455.792 = 592.54 mm2 From Steel table, Select double angle
Taking minimum size that is 2ISA 50 x 50 x 6 mm Area = 1136 mm2
Also rxx = 15.1 mm and ryy = 24.6 mm (For a gap of 10 mm) b. Design of Connections:
Given M 16 bolts, Assume grade 8.8 HSFG bolts
1
Vdsf = 
𝑚𝑓
[μf ne Kh Fo], μf = 0.55, ne = 2, Kh = 1 and
o
F =0.7 *fu * An = 0.7*800*
𝜋∗ 16
2
4
= 87.82 x 103 N
dsf
V =
1
1.25
[0.55 * 2 * 1 *87.823 x103]
Vdsf
= 77.284 KN
Therefore Bolt Value = 77.284 KN
No. of Bolts =
=
𝐹𝑜𝑟𝑐𝑒 89.71
𝐵𝑜𝑙𝑡 𝑉𝑎𝑙𝑢𝑒 77.284
= 1.16 Say 2 nos
 Number of bolts = 2 nos.
3

## Slide 77
4

## Slide 78
5

## Slide 79
6

## Slide 80
7

## Slide 81
8

## Slide 82
9

## Slide 83
10

## Slide 84
11

## Slide 85
b. Thickness of Base Plate:
o
𝐴𝑟𝑒𝑎 200 𝑥 200
𝐿𝑜𝑎𝑑 270∗ 10^3
q = = = 6.75 mm2
Considering 1 m strip, qo / meter = 2.25 x 1 = 6.75 N/mm
Moment along x -x
Mx-x = 6.75 *80*80/2 = 21,600 N-mm
Equating Mx-x = Md
= 1.2 Ze
𝑓𝑦
𝛾𝑚𝑜
…. Page 53 IS – 800
21,600 = 1.2 Ze
250
1.10
𝐼
3
Where Ze = = (bd /12)/(d/2)
𝑦
=bd2/6 = (1mm *(t+8)2)/6
21600 = 1.2 (1mm *(t+8)2)/6 ∗
250
1.10
t = ……… mm . … . 𝑚𝑚
∴ Provide base slab 200 mm x 200mm x ………mm
12

## Slide 86
c. Anchor Bolts:
Given uplift force = 50 KN Provide 4 bolts at each end.
∴ Force in each bolt = 50/4 = 12.5 KN Ultimate force = 1.4 * 4 = 18.75 KN
From IS 456, for M20 Concrete
(τbd )bond stress = 1.2 N/mm2 * 1.60 …….Page No. 43 Equating external force = Resisting force
18.75 KN = Circumference of bolt * Height * Bond Stress
18.75 = π D * h * τbd
18.75 * 103 = π * 16 * h * 1.2 * 1.6
h = ……… mm ≈ ⋯ … … . 𝑚𝑚 Hence Provide at each end 4-16mm dia,...….. mm length anchor bolts
13

## Slide 87
14

## Slide 88
15

## Slide 89
Roof Truss type 2 – 2nd Problem
2. The forces in the members of the roof truss of an
industrial building are as shown in table. The truss is supported on 400mm thick masonry. End reaction due to dead load + live load is 10.556 KN. Members are to be connected at the joints with 16 mm dia bolts and 8mm thick gusset plate. Design the members and base plate. Assume permissible bearing pressure on masonry = 0.8 Kn/mm2 and size of the Shoe angle is 2ISA 75 x 75 x 6mm on each side of the gusset plate.
Members | Force | 
 | Compression (-ve) KN | Tension (+ve) KN
LoV1,V1V2,V2V3 | -17.4 | 20.9
LoL1, L1L2, L2L3 | -14 | 14.9
V3L2 | -8.7 | 6
V2L2 | -5.3 | 7.4
V2L1 | -6.7 | 4.6
V1L1 | -3.5 | 5
16

## Slide 90
17
Soln:
1. Load Calculation:
Members | Force |  | Final Design Force | Length in m
 | Compression (-ve) KN | Tension (+ve) KN |  | 
LoV1,V1V2,V2V3 | -17.4 | 20.9 | Top Chord +20.9 (T) -17.4 (C) | 1.79
LoL1, L1L2, L2L3 | -14 | 14.9 | Bottom Chord +14.9 (T) -14 (C) | 3.10
V3L2 | -8.7 | 6 | Inner Member +8.7 (C) -7.4 (T) | 3.10
V2L2 | -5.3 | 7.4 |  | 
V2L1 | -6.7 | 4.6 |  | 
V1L1 | -3.5 | 5 |  | 
Design Top Chord Member:
Since tension force is more than compressive force, Design the member as tension member and check for Compressive load Carrying Capacity
Desing of Bottom Chord Member:
Since tension force is more than compressive force, Design the member as tension member and check for Compressive load Carrying Capacity
Desing of Inner Member:
Since Compressive force is more than tension force, Design the member as Compressive member and check for Tension load Carrying Capacity

## Slide 91
Design of Base Plate: ( Design of Support)
  Area of Base Plate
  Thickness of Base Plate c . Anchor Bolts
3. Design a roof truss shown in figure. The forces in the members of the truss due to dead load, live load and wind load are tabulated below.
18

## Slide 92
19
Soln:
1. Load Calculation:
Members | DL + LL (KN) | DL+WL (KN) | Design Force (KN) | Length in M
AB | +36.17 | -22.95 | Top Chord +36.17 (C) -23.85 (T) | 1.863
BC | +29.24 | -20.44 |  | 
CD | +30.31 | -23.85 |  | 
DE | -12.83 | +9.57 | Inner Member -12.83 (C) +9.57 (T) | 3.33
EC | +6.95 | -5.65 |  | 
EB | +6.95 | -6.38 |  | 
EA | -32.21 | +18.84 | Bottom Chord - 32.21 (C) + 18.84 (T) | 3.33
EF | -19.30 | +7.94 |  | 
Design of Top Chord Member
Design of Bottom Chord Member
Design of Inner Member

## Slide 93
Welded Plate Girder and its Components:
Page 1 of 16

## Slide 94
Page 2 of 16
Module 2
Design of Welded Plate Girder
Plate girders are deep built-up beams used in bridges, building and industrial structure. For heavy loads and long spans, plate girders are substituted for rolled beams. A Plate girder consists of web plate with stiffeners if required and top & bottom flanges.
Components of Welded Plate Girders:
Following are the various components of plate girder as shown in the figure.
Flange plates: Top and Bottom Plates to take the bending moment.
Web Plate: To take the shear force.
Vertical or Transverse Stiffeners: Provided along the span to increase web buckling strength.
Horizontal Stiffeners or Longitudinal stiffeners: Provided in areas of very high moments.
End or Bearing Stiffeners: Provided at Concentrated loads and reactions points to transfer the loads.
Splices: They are provided if necessary continuity required in the web & flanges.

## Slide 95
Following are the different steps used in design of Welded plate Girder:
Design of mid span
  Load Calculation
  Girder Dimensions
    Web Depth
    Web Thickness
    Flange width
    Flange Thickness
  Check for moment of resistance
  Check for Shear
  Welded connection between flange and Web
Curtailment of flange plate
Design of Intermediate Stiffeners (IS)
Design of End Bearing Stiffeners (EVS)
Page 3 of 16

## Slide 96
Page 4 of 16

## Slide 97
Page 5 of 16

## Slide 98
Page 6 of 16

## Slide 99
Page 7 of 16

## Slide 100
Page 8 of 16

## Slide 101
Page 9 of 16

## Slide 102
Page 10 of 16

## Slide 103
Page 11 of 16

## Slide 104
Page 12 of 16

## Slide 105
Page 13 of 16

## Slide 106
Page 14 of 16

## Slide 107
Page 15 of 16

## Slide 108
Page 16 of 16